## Slide 1: Team 2
Instruction Set and Initialization

## Slide 2: Current Instruction Set
NOOP
ADD
INC
SLT
ADDI
INCI
SLTI
BEQ
LW
SW
JAL
J
JR
All instructions are 16 Bits

## Slide 3: Initialization
Assumptions:
1 - The program counter is hardware initialized to zero when the processor first gets power.
2 - The start of this initialization program is located at the zeroth index in the instruction memory (ROM)
3 – Start a program to set clock to 12:00AM

## Slide 4: Initialization
00 ADD $zero, $zero, $s0
01 ADD $zero, $zero, $s1
02 ADD $zero, $zero, $s2
03 ADD $zero, $zero, $s3
04 ADD $zero, $zero, $s4
05 ADD $zero, $zero, $s5
06 ADD $zero, $zero, $s6
07 ADD $zero, $zero, $t0
08 ADD $zero, $zero, $t1
09 ADD $zero, $zero, $a0
10 ADD $zero, $zero, $a1
11 ADD $zero, $zero, $vo
12 ADD $zero, $zero, $ra
13 J START_OF_PROGRAM
00 Init $s0 to 0
01 Init $s1 to 0
02 Init $s2 to 0
03 Init $s3 to 0
04 Init $s4 to 0
05 Init $s5 to 0
06 Init $s6 to 0
07 Init $t0 to 0
08 Init $t1 to 0
09 Init $a0 to 0
10 Init $a1 to 0
11 Init $v0 to 0
12 Init $ra to 0
13 Jump to clock program

## Slide 5: Current Instruction Set
NOOP
  0000 0000 0000 0000
  No operation command
ADD $Rd, $Rs, $Rt
  0001 ssss tttt dddd
  Will add Rs to Rt and store in Rd
INC $Rd, $Rs
  0010 ssss dddd dddd
  Increment Rd by Rs and store in Rd

## Slide 6: Current Instruction Set
SLT $Rd, $Rs, $Rt
  0011 ssss tttt dddd
  Checks if Rs < Rt then store in Rd
ADDI $Rd, $Rs, IMM
  0100 ssss tttt dddd
  Add Immediate
INCI $Rt, IMM
  0101 tttt tttt iiii
  Increment immediate

## Slide 7: Current Instruction Set
SLTI $Rt, $Rs, IMM
  0110 ssss tttt iiii
  Checks Rs < IMM then stores in Rt
BEQ $Rs, $Rt, IMM
  0111 ssss tttt iiii
  If Rs = Rt then go to IMM
LW $Rt, IMM ($Rt)
  1000 ssss tttt iiii
  Gets memory(Rs + IMM) and puts into Rt

## Slide 8: Current Instruction Set
SW $Rt, IMM ($Rt)
  1001 ssss tttt iiii
  Stores Rt into Memory(IMM + Rt)
JAL IMM
  1010 iiii iiii iiii
  Jumps to IMM and stores PC into JR
J IMM
  1011 iiii iiii iiii
  Jump to immediate field
JR $Rs
  1100 ssss 0000 0000
  Jump to the return address

## Slide 9: Current Instruction Set
AND (Bitwise and) $Rd, $Rs, $Rt
  1101 ssss tttt dddd
  Bitwise AND $Rs & $Rt stores result $Rd
OR (Bitwise or) $Rd, $Rs, $Rt
  1110 ssss tttt dddd
  Bitwise OR $Rs | $Rt stores result $Rd